Processor-- STM32F446RET6 (512K flash, 3 CAN 2.0)
- check power pinouts: maybe layout could accommodate G483 (3 CAN), F405/4 (2 CAN), F103 (2 CAN)

Processor Outputs
1. Three CAN
- non-isolated 12v power
- isolation option (provision for a 3w isolation dc-dc for the 12v?)
2. 12v power switch (FETs) on each CAN, or just one?
3. CAN bus reset line(s)
4. Two chargers external relay on/off
5. Generator?
Item: generator control might better be a separate node controlled via CAN. E.g. auto-start, shut-down, …
6. uart- console monitor/debugging
7. uart- CAN hub-CAN hub comm, or Rpi comm
8. JIC FETs as pins & layout permit.

Processor Inputs
1. Pushbutton: wake up
2. pushbutton(s): display/function-selection

Processor Display
1. 12v power led: green
2. I/o leds
- red
- green
3. I2C lcd display

Processor ADC
1. 12v voltage
2. 12v current (Hall-effect sensor)?

12v Power –
- Multiple 12v? If so, diode, or FET, OR’ed?
- Spade lugs?
- Fuse ground? (JIC battery polarity reversed and there is a separate ground)
- 12v power to processor always present so that RTC can wake up processor?
- And/or CR2032 coin battery for Vbat? On PCB or external?

CAN connectors--
- Stacked in/out D connectors?
- 2x5 ribbon header?
- RJ45 jack pair?